## Slide 1: ECE 383 – Embedded Computer Systems II Lecture 18 – MicroBlaze + Custom IP
Capt Jeffrey Falkinburg Room 2E46C 333-7366
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Time Logs!
MicroBlaze + Custom IP

## Slide 3: MicroBlaze + Custom IP

## Slide 4: MicroBlaze + Custom IP

## Slide 5: MicroBlaze + Custom IP – Workflow
The work flow has two main steps.
  Define the hardware (microBlaze + custom IP) in EDK
  Program the resulting hardware in the SDK environment.
Lets start with the first step.

## Slide 6: Xilinx Platform Studio – EDK
This step requires that you defined the logical arrangement of the component in VHDL. Your entity description will contain two types of connections; those targeted at external ports on the Spartan6 chip and those intended to be accessible to the microBlaze processor.
Start new project called Lecture_18 and add the axi_uartlite
  Base address

## Slide 7: Xilinx Platform Studio – EDK
Start new project called Lecture_18 and add the axi_uartlite
  Set base address to
Lecture 18 then says “Create first repository”

## Slide 8: MicroBlaze + Custom IP

## Slide 9: Xilinx Platform Studio – EDK
Add component from repository to project
Configure component
  Base address

## Slide 10: Xilinx Platform Studio – EDK
Connections to microBlaze
  Add signals to user_logic port
  For outputs: slv_regX <= signal;
  For inputs: signal <= slv_regX;
Connections off chip
  Add ports to Microprocessor Peripheral Definition (.mpd) file
  Add signals to user_logic.vhd port
  Add signals to counter.vhd port
  Add ports to master.ucf file

## Slide 11: Xilinx Platform Studio – EDK

## Slide 12: Custom IP
In Xilinx Platform Studio, go to Hardware → Create or Import Peripheral

## Slide 13: Custom IP

## Slide 14: Custom IP

## Slide 15: Custom IP
IP_Repo Folder should be in Bitbucket Repo

## Slide 16: Custom IP

## Slide 17: Custom IP

## Slide 18: Custom IP

## Slide 19: Custom IP

## Slide 20: Custom IP

## Slide 21: Custom IP

## Slide 22: Custom IP

## Slide 23: Custom IP

## Slide 24: Custom IP

## Slide 25: MicroBlaze + Custom IP

## Slide 26: Modify *.mpd
    The *.mpd file can be used to specify “ports” that will be connected to FPGA pins under the “Ports” tab of XPS.

## Slide 27: Modify *.mpd
    The *.mpd file can be used to specify “ports” that will be connected to FPGA pins under the “Ports” tab of XPS.
    PORT LED = "", DIR = O, VEC=[7:0]

## Slide 28: Part 1a: Hardware Questions/ Notes related to handout
Note: the truth table for the counter is in the comments.
Q: In lec18.vhdl, what other library must be added?
Q: In lec18.vhdl, does the use work.lec18Parts.all library need to be added?

## Slide 29: Lec18.vhdl – Counter

## Slide 30: Download Pack File and lec18.vhd
Add Lecture 18 Pack file (lec18_pack.vhdl) and lec18.vhdl to pcore vhdl folder using this path:
  Path_to_repo\IP_Repo\MyProcessorIPLib\pcores\counter_v1_00_a\hdl\vhdl\

## Slide 31: MicroBlaze + Custom IP

## Slide 32: Modify *.pao
Add the lec18_pack.vhdl and lec18.vhdl to the *.pao
The *.pao file lists all the VHDL files you need to build your peripheral. If you add a separate file (e.g., video synchronization), you need to list it in this file. Order matters, so place the dependent files last.
  lib counter_v1_00_a lec18_pack.vhdl
  lib counter_v1_00_a lec18.vhdl

## Slide 33: Part 1b: Hardware Questions/ Notes related to handout
Q: In user_logic.vhd, what do the generics C_NUM_REG, C_SLV_DWIDTH do?
Q: In user_logic.vhd, what two roles is slv_reg0 serving?
Q: In user_logic.vhd, what roles does slv_reg1 serve?
Q: In user_logic.vhd, slv_reg0 is on the left and right-hand side of an assignment. Identify the two lines where this happens.
Q: In user_logic.vhd, on line 62, what is the role does X"000000" serve?

## Slide 34: User_logic.vhd

## Slide 35: MicroBlaze + Custom IP

## Slide 36: User_logic.vhd
Add lec18Parts to user_logic
use IEEE.NUMERIC_STD.ALL;
use work.lec18Parts.all;

## Slide 37: User_logic.vhd
Add User Port for LEDs

## Slide 38: User_logic.vhd
Add User Signal for Q

## Slide 39: User_logic.vhd
Add Counter Port Map and LED assignment for user logic
counter: lec10
generic map (8)
port map( clk => Bus2IP_Clk,
reset => Bus2IP_Resetn,
ctrl => slv_reg1(1 downto 0),
D => unsigned(slv_reg0(7 downto 0)),
Q => Q);
LED <= std_logic_vector(Q);

## Slide 40: User_logic.vhd
Add read signal Q on slv_reg0 when using 8 slave registers:
case slv_reg_read_sel is
when "10000000" => slv_ip2bus_data <= X"000000" & std_logic_vector(Q);

## Slide 41: MicroBlaze + Custom IP

## Slide 42: Part 1c: Hardware Questions/ Notes related to handout
Q: If you want a signal to go outside the Spartan chip...
  What files must it appear on the entity description?
  What other files must contain information about the signal?
Q: If you want a signal to go to the microBlaze...
  What files must it appear on the entity description?
  In order for the microBlaze to read the signal, what must you do?
  In order for the microBlaze to write to the signal, what must you do?

## Slide 43: Counter.vhd

## Slide 44: Counter.vhd

## Slide 45: Counter.vhd

## Slide 46: System.ucf
Add UART Lite pins and LED pins to System.ucf
  # UART Lite Tx/Rx pins
  net axi_uartlite_0_RX_pin LOC=A16 | IOSTANDARD = LVCMOS33;
  net axi_uartlite_0_TX_pin LOC=B16 | IOSTANDARD = LVCMOS33;
  # LED_pins
  net LED_pin(7) LOC=N12 | IOSTANDARD = LVCMOS33;
  net LED_pin(6) LOC=P16 | IOSTANDARD = LVCMOS33;
  net LED_pin(5) LOC=D4 | IOSTANDARD = LVCMOS33;
  net LED_pin(4) LOC=M13 | IOSTANDARD = LVCMOS33;
  net LED_pin(3) LOC=L14 | IOSTANDARD = LVCMOS33;
  net LED_pin(2) LOC=N14 | IOSTANDARD = LVCMOS33;
  net LED_pin(1) LOC=M14 | IOSTANDARD = LVCMOS33;
  net LED_pin(0) LOC=U18 | IOSTANDARD = LVCMOS33;

## Slide 47: Adding Custom IP

## Slide 48: Adding Custom IP

## Slide 49: Adding Custom IP

## Slide 50: Adding Custom IP

## Slide 51: Adding Custom IP

## Slide 52: Adding Custom IP
Increase BRAM size to 16k or 64k
Set Counter address to 0x83000000
Set axi_uartlite_0 address to 0x84000000

## Slide 53: Export Design
Export Design and take a coffee break while it builds

## Slide 54: Part 1: Hardware Questions/ Notes related to handout
Note: the truth table for the counter is in the comments.
Q: In lec18.vhdl, what other library must be added?
Q: In lec18.vhdl, does the use work.lec18Parts.all library need to be added?
Q: In user_logic.vhd, what do the generics C_NUM_REG, C_SLV_DWIDTH do?
Q: In user_logic.vhd, what two roles is slv_reg0 serving?
Q: In user_logic.vhd, what roles does slv_reg1 serve?
Q: In user_logic.vhd, slv_reg0 is on the left and right-hand side of an assignment. Identify the two lines where this happens.

## Slide 55: Part 1: Hardware Questions/ Notes related to handout
Q: In user_logic.vhd, on line 62, what is the role does X"000000" serve?
Q: If you want a signal to go outside the Spartan chip...
  What files must it appear on the entity description?
  What other files must contain information about the signal?
Q: If you want a signal to go to the microBlaze...
  What files must it appear on the entity description?
  In order for the microBlaze to read the signal, what must you do?
  In order for the microBlaze to write to the signal, what must you do?

## Slide 56: Export Design
Export & Launch SDK…assuming no errors

## Slide 57: Export to SDK Folder

## Slide 58: New SDK Project

## Slide 59: New SDK Project

## Slide 60: New C Source File

## Slide 61: New C Source File

## Slide 62: Lec18.c

## Slide 63: Lec18.c

## Slide 64: Part 2: Software Questions/ Notes related to handout
Why doesn't the 'c' command cause the counter to count up by 1?
On line 46, why did I subtract 0x30?
After loading the counter on line 48, something should be done that is missing.
What line of VHDL code in user_logic.vhd is "activated" when line 28 executes?
What line of VHDL code in user_logic.vhd is "activated" when line 53 executes?
What line of VHDL code in lec18.vhdl "activated" when line 53 executes?
What appears to be the naming convention for hardware registers?

## Slide 65: Add C code to Source File
#include <xuartlite_l.h> // Contains XUartLite_RecvByte
#include <xparameters.h>
#include <xil_io.h> // Contains Xil_Out8 and its variations
#include <stdio.h> // Contains xil_printf
#define uartReadReg 0x84000000 // read <= RX, write=>TX
#define countQReg 0x83000000 // 8 LSBs of slv_reg0 read=Q, write=D
#define countCtrlReg 0x83000004 // 2 LSBs of slv_reg2 are control
#define count_HOLD 0x00 // The control bits are defined in the VHDL
#define count_COUNT 0x01 // code contained in lec18.vhdl. They are
#define count_LOAD 0x02 // added here to centralize the bit values in
#define count_RESET 0x03 // a single place.
int main(void) {
u8 c;
while(1) {
c=XUartLite_RecvByte(uartReadReg);
switch(c) {
//-------------------------------------------------
// Reply with the help menu
//-------------------------------------------------
case '?':
xil_printf("--------------------------\r\n");
xil_printf(" count Q = %x\r\n",Xil_In16(countQReg));
xil_printf("--------------------------\r\n");
xil_printf("?: help menu\r\n");
xil_printf("o: k\r\n");
xil_printf("c: COUNTER count up LEDs (by 9)\r\n");
xil_printf("l: COUNTER load counter\r\n");
xil_printf("r: COUNTER reset counter\r\n");
xil_printf("f: flush terminal\r\n");
break;
//-------------------------------------------------
// Basic I/O loopback
//-------------------------------------------------
case 'o':
xil_printf("k \r\n");
break;
//-------------------------------------------------
// Tell the counter to count up
//-------------------------------------------------
case 'c':
Xil_Out8(countCtrlReg,count_COUNT);
Xil_Out8(countCtrlReg,count_HOLD);
break;
//-------------------------------------------------
// Tell the counter to load a value
//-------------------------------------------------
case 'l':
xil_printf("Enter a 0-9 value to store in the counter: ");
c=XUartLite_RecvByte(uartReadReg) - 0x30;
Xil_Out8(countQReg,c); // put value into slv_reg1
Xil_Out8(countCtrlReg,count_LOAD); // load command
xil_printf("%c\r\n",c+0x30);
break;
//-------------------------------------------------
// Reset the counter
//-------------------------------------------------
case 'r':
Xil_Out8(countCtrlReg,count_RESET); // reset command
break;
//-------------------------------------------------
// Clear the terminal window
//-------------------------------------------------
case 'f':
for (c=0; c<40; c++) xil_printf("\r\n");
break;
//-------------------------------------------------
// Unknown character was
//-------------------------------------------------
default:
xil_printf("unrecognized character: %c\r\n",c);
break;
} // end case
} // end while 1
return 0;
} // end main

## Slide 66: Add C code to Source File
while(1) {
c=XUartLite_RecvByte(uartReadReg);
switch(c) {
//-------------------------------------------------
// Reply with the help menu
//-------------------------------------------------
case '?':
xil_printf("--------------------------\r\n");
xil_printf(" count Q = %x\r\n",Xil_In16(countQReg));
xil_printf("--------------------------\r\n");
xil_printf("?: help menu\r\n");
xil_printf("o: k\r\n");
xil_printf("c: COUNTER count up LEDs (by 9)\r\n");
xil_printf("l: COUNTER load counter\r\n");
xil_printf("r: COUNTER reset counter\r\n");
xil_printf("f: flush terminal\r\n");
break;

## Slide 67: Add C code to Source File
//-------------------------------------------------
// Basic I/O loopback
//-------------------------------------------------
case 'o':
xil_printf("k \r\n");
break;
//-------------------------------------------------
// Tell the counter to count up
//-------------------------------------------------
case 'c':
Xil_Out8(countCtrlReg,count_COUNT);
Xil_Out8(countCtrlReg,count_HOLD);
break;
//-------------------------------------------------
// Tell the counter to load a value
//-------------------------------------------------
case 'l':
xil_printf("Enter a 0-9 value to store in the counter: ");
c=XUartLite_RecvByte(uartReadReg) - 0x30;
Xil_Out8(countQReg,c); // put value into slv_reg1
Xil_Out8(countCtrlReg,count_LOAD); // load command
xil_printf("%c\r\n",c+0x30);
break;

## Slide 68: Add C code to Source File
//-------------------------------------------------
// Reset the counter
//-------------------------------------------------
case 'r':
Xil_Out8(countCtrlReg,count_RESET); // reset command
break;
//-------------------------------------------------
// Clear the terminal window
//-------------------------------------------------
case 'f':
for (c=0; c<40; c++) xil_printf("\r\n");
break;
//-------------------------------------------------
// Unknown character was
//-------------------------------------------------
default:
xil_printf("unrecognized character: %c\r\n",c);
break;
} // end case
} // end while 1
return 0;
} // end main

## Slide 69: Xilinx Software Development Kit - SDK
In the SDK environment, you program the hardware built in the previous step.
The key concept here is that the peripheral defined in EDK are accessible through the slave registers as memory mapped devices.
For example, I assigned counter_0 to have a BaseAddress 0x83000000. In the user_logic.vhdl file, I (arbitrarily) assigned counter ports to slave register according to the table below.
Signal | direction | Slave Register | Address
D | input | slv_reg0(7 downto 0) | 0x83000000
ctrl | input | slv_reg1(1 downto 0) | 0x83000004
Q | output | slv_reg0(7 downto 0) | 0x83000000

## Slide 70: Increase Stack and Heap Size

## Slide 71: Configure JTAG Settings
Go to Xilinx Tools → Configure JTAG Settings (You may get a pop-up requesting admin access for this step)
Under “Type,” select “Digilent USB Cable” and then click “OK” (You have to do this for every new project!)
71

## Slide 72: Build and Export to FPGA
72

## Slide 73: MicroBlaze + Custom IP